## Slide 1
Innovative Evaluation Practices for
BCSE308P Computer Networks Lab
Fall Semester 2026-27
CCSDS INSPIRED SOFTWARE TELEMETRY
RECEIVER AND GROUND STATION
24BCE2055 JAHNAVI SINGH
Submitted to: SREETHAR S.
Notes: Sir, the basic idea is to simulate space telemetry. Telemetry means sending measurements from a remote system to a receiving station. Here, our spacecraft is a program generating mock readings. We focus on how the receiver finds frames, checks them, and continues after damage.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 2
Frame boundaries and arriving messages
A telemetry frame can span several arriving messages.
One message can contain the end of one frame and the start of another.
The receiver must recover boundaries after corruption or a bit slip.
Logical frames
Frame A
Frame B
UDP datagrams
Part 1
Part 2
Part 3
Part 4
Part 5
Part 3 crosses the frame boundary
Our packetizer creates the chunks. UDP carries each chunk as one datagram.
Notes: We cannot assume that each incoming message is a complete frame. We deliberately divide the logical stream into chunks before sending it through UDP. The receiver gets those chunks intact, but it must discover the telemetry boundaries itself. This is application-level framing. Using TCP would not remove the need to define those boundaries either.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 3
System architecture
Mock spacecraft
transmitter
Ground-station
receiver
Ground-station
browser UI
Generate mock readings
Build frame, CRC and ASM
Inject selected bit fault
Packetize the bitstream
Preserve incoming bits
Find ASM at any bit
Check CRC and format
Decode accepted readings
Incoming chunks
State transitions
CRC and alignment
Accepted readings
UDP
WebSocket
UDP carries telemetry chunks. WebSocket carries receiver observations.
Notes: There are three main parts. The transmitter creates the mock data and sends it. The receiver does the actual synchronization and validation work. The UI helps us see that work. UDP carries the telemetry chunks; WebSocket carries the receiver's observations to the browser.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 4
Telemetry transmission unit
260 bytes = 2,080 bits
ASM
4 bytes
Sequence
4 bytes
Length
2 bytes
Flags
2 bytes
Payload + padding
246 bytes
CRC-16
2 bytes
Custom frame body: 256 bytes
Complete transmission unit: 260 bytes
ASM marks a possible start. Sequence, length and flags form the 8-byte header.
The default payload contains 12 telemetry bytes and 234 zero-padding bytes.
The CRC is an additional check value. Readings remain in the payload.
Notes: This is similar to a packet-format diagram, but it shows the entire unit. The readings become payload bytes. We add a sequence number, length, flags, and CRC to make a 256-byte body. Then we prepend a four-byte start marker. CRC is not a replacement for the readings; it is a check value included alongside them.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 5
Persistent buffering between arrivals
The buffer retains unfinished data between datagrams.
New bits are appended. Processed bits are consumed or discarded.
A complete candidate needs 2,080 bits, starting at its ASM.
33 B
48 B
57 B
48 B
Persistent bit buffer
1,752 retained bits + 384 new bits = 2,136 available bits
2,080 candidate bits
56 extra bits
Hypothetical clean candidate: 56 bits remain after a valid unit is consumed
00000000 00000001 00000000 00001100 00000000 00000000 00001001 01100101
Notes: Think of separate envelopes bringing pieces of a letter. These boxes are the envelopes; the buffer is the table where we keep their contents. We do not throw away a partial frame when a message ends. In this example, the new arrival gives us enough bits to check a complete candidate. Persistent means retained between arrivals while the receiver runs, not permanently saved to disk.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 6
Attached Sync Marker search
ASM is a fixed 32-bit marker: 0x1ACFFC1D
Exact marker bits
0
0
0
1
1
0
1
0
1
1
0
0
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
1
1
1
0
1
Same marker beginning one bit later in a schematic stream
0
0
0
0
1
1
0
1
0
1
1
0
0
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
1
1
1
0
1
Compare a 32-bit window
No match: advance one bit
Match: collect candidate
Marker matches
Repeat comparison
The marker can cross byte or datagram boundaries. CRC and format checks still follow.
Notes: ASM is a start sign in the incoming bits. The receiver checks 32 consecutive bits against this known pattern. If they do not match, it moves by one bit and tries again. A match tells us where a possible frame starts, but it does not prove that the following data is valid.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 7
Receiver finite-state machine
HUNT
Search for the ASM
LOCK
Wait for 2,080 bits
VERIFY
Check CRC and length
EXTRACT
Accept and decode
ASM found
Enough bits
CRC and format
pass
CRC or format fails: discard one bit, then search again
Next ASM already at head
No complete next marker at head: return to HUNT
Notes: The four states are simple: find, wait, check, and accept. HUNT finds the marker. LOCK waits for the rest. VERIFY checks the candidate. EXTRACT accepts the readings. If checks fail, we return to searching. If extraction finishes and the next marker is already buffered, we can go directly back to LOCK.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 8
Marker alignment inside a byte
08
Alignment is the marker start position modulo 8
Byte boundary: alignment 0
Last bit of a byte: alignment 7
0
Start
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
Start
Marker starts at the first bit
Marker continues into later bytes
Stream bit 4,160 has alignment 0 because 4,160 mod 8 = 0.
Stream bit 8,319 has alignment 7 because 8,319 mod 8 = 7.
Alignment does not identify a frame number or the damaged bit.
Notes: The 0–7 row confused me initially, so this distinction matters. A highlighted zero does not mean frame zero. It means the marker starts at the first bit of a byte. For example, the candidate at stream bit 4160 has alignment zero because 4160 is divisible by eight. Alignment also does not tell us which bit was corrupted.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 9
CRC validation and decoded telemetry
CRC = Cyclic Redundancy Check
Received
candidate body
CRC and format check
0x6AA9 = 0x6AA9
Example frame 656
24.56 °C
7,404 mV
520,656 m
656 s simulated uptime
Rejected candidate
Resume marker search
CRC differs
Only accepted frames update the displayed readings.
A matching CRC means no corruption was detected. It does not repair data.
Notes: The receiver does the same CRC calculation on the received body and compares the result with the transmitted value. If CRC and format pass, it decodes the bytes into readable measurements. The space-telemetry connection is these measurements about the spacecraft's condition. Here they are mock values. Our simulated uptime is generated from the sequence number, not actual elapsed program time. CRC detects damage; it does not fix it or locate the exact bad bit.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 10
Recovery after a damaged candidate
The receiver rejects the candidate and keeps running
Frame 1
Accepted
Frame 2
Damaged candidate
Frame 3
Accepted after recovery
Failed candidate ASM
begins at bit k
Resume HUNT
at bit k + 1
Find a later ASM
and validate normally
Bit-by-bit search through the remaining buffered data
Search restarts one bit after the failed marker, not 2,080 bits later.
Recovery skips damaged readings. It does not reconstruct them.
Notes: This is the main recovery feature. If CRC fails, we do not terminate the receiver. We also do not assume where the next frame begins. We resume the bit-level search one bit after the failed candidate's marker. We then find another marker and validate its frame. Once a valid frame is found, decoding continues. The damaged readings are skipped, not repaired.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 11
Effects of the guided experiments
Experiment | Change in the logical stream | Later alignment
Clean | No fault, with normal chunk boundaries | 0
Start between bytes | Prefix three bits before the stream | 3
Flip one bit | Change one value without changing bit count | 0 then 0
Insert one bit | Add one bit and move later starts forward | 0 then 1
Delete one bit | Remove one bit and move later starts backward | 0 then 7
Schematic edits to original bits 1 0 1 1 0 0
Flip
1 0 [0] 1 0 0
Insert
1 0 [1] 1 1 0 0
Delete
1 0 [ ] 1 0 0
Six-frame clean / offset runs: 6 accepted, 0 CRC failures
Flip / insert / delete: 5 accepted, 1 CRC failure, 1 gap, 1 reacquisition
Notes: All three faults damage frame 2, but their effects on later frames differ. A flip changes a value without moving boundaries. An insertion pushes later starts one bit forward. A deletion pulls them one bit backward, which appears as alignment seven. The receiver observes markers, checks, and positions; it is not told which fault happened. The selected experiment tells us the injected cause.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md

## Slide 12
Demonstration workflow
1 Clean transmission
Buffer fills and a frame passes
2 Flip one bit
CRC mismatch rejects frame 2
3 Insert one bit
Alignment 1 and valid frames resume
Controls: Restart, Play/Pause, Step, Next state, and playback speed
Guided lab processes a six-frame recording in memory through the same receiver engine.
Live mode receives actual localhost UDP datagrams and publishes observations over WebSocket.
Terminal 1
npm run receiver
Terminal 2
npm run ui
Browser
http://127.0.0.1:5173
Optional Terminal 3 for Live: npm run transmitter -- --mode clean
The receiver continues decoding later valid frames without restarting
Notes: I will first use Guided lab because we can pause each transition. Next state skips to the next FSM change; Step advances one recorded step. Playback speed changes the walkthrough speed, not the network rate. We will compare a clean run, a flipped bit, and an inserted bit. Then I can switch to Live to show actual UDP traffic. The result is a receiver that finds and validates frames even when message boundaries do not match frame boundaries, and continues receiving after damage without restarting.
Source: D:/jenevi/FALL SEM 26-27/CN/Project/docs/presentation-content.md
Demonstration notes
- Guided lab needs the receiver and UI, but no running transmitter. Its recording uses the same frame builder, simulator, packetizer, synchronizer, and CRC implementation, with chunks processed in memory.
- Select an experiment and press Restart before explaining it. At “complete,” use Latest valid alignment to discuss the recovered frames; current alignment may be absent because the receiver has returned to HUNT.
- Pause at a rejected candidate to show the unequal CRC values. Then continue to a later accepted frame and inspect Latest valid alignment.
- The 0–7 row is alignment. The small chunk numbers are arrival counters. Frame sequence is a third, separate identifier.
- During guided playback, the FSM can pause within a chunk while buffer counters update at chunk completion. Do not treat a before-chunk bar and an end-of-chunk caption as a single instantaneous snapshot.
- A sequence gap counts missing accepted frame observations, not missing UDP datagrams. Reacquisition counts a marker found after a rejected candidate; startup acquisition alone does not count.
- The live receiver runs independently of the browser. Closing the dashboard or freezing its visuals does not stop UDP reception.
- For a fresh live fault demonstration, stop the old transmitter, restart the receiver to reset counters, and run `npm run transmitter -- --mode bit-insert --target-frame 50`. At the default 5 frames/second the fault occurs roughly ten seconds into transmission. Do not restart during the fault.
- Conclude with the scope: software-only, mock measurements, custom educational frame body; no RF hardware, retransmission, forward error correction, or repair of rejected readings.